Developing an IoT System
IoT Air Quality System
Uli Raich (uli.raich@gmail.com)
The DHT11 temperature and humidity sensor
Presented at the Workshop – IoT4AQ
March 2024, Bambey, Sénégal

---
DHT11 sensor
The DHT11 is a popular temperature and humidity sensor
It contains the sensors, analogue to digital conversion and a processor sending the measurement results over its own proprietary serial protocol
It uses only 3 pins:
- Vcc (3.3V)
- GND
- Data

---
The humidity sensor
- Variations in relative humidity produce a change
  of resistivity, which is measured.
- The resistance of certain hygroscopic materials such as
  hygroscopic salts have such a property
- These materials are mounted as thin films on
  the substrate with metal contacts
- The devices can be very small

---
The temperature sensor

---
The connections

---
Communication process
- The processor initiates a measurement cycle pulling the data line down for 18 ms (data line is output to the CPU)
- It releases the line and waits for 20-40 µs (data line now input)
- The DHT11 sends a 80 µs start signal
- 40 data bits follow: 26-28 µs : zero, 70 µs one

---
The full protocol
- Humidity integral
- Humidity decimal
- Temperature integral
- Temperature decimal
- Checksum

---
DHT11 library
The DHT11 library implements the DHT11 driver as a C++ class.
Classes incorporate data as well as functions (called methods) in a single module. Classes can inherit code from super classes.
In order to use a class you must create an object of the class:
#define DHT11_DATALINE 23
DHT11 dht11(DHT11_DATALINE);
Then you can use the object in the loop function.
dht11.readTemperature() and dht11.readHumidity() return the measured values or an error code, if something goes wrong
You must wait for 1 s in between two measurements

---
DHT11 errors
You can have 2 types of errors:
- Timeout: The DHT11 does not react on a measurement request (wrong cabling?)
- There may be a checksum error
You can check for DHT11::ERROR_TIMEOUT or DHT11::ERROR_CHECKSUM
and you can print a human readable error message with:
Serial.println(dht11.getErrorString(temperature)); // or humidity

---
Reading temperature and humidity