Developing an IoT System
IoT Air Quality System
Uli Raich (uli.raich@gmail.com)
Introduction to the hardware
Presented at the Workshop – IoT4AQ
March 2024, Bambey, Sénégal

---
Resources
The slides and the code of all demo programs are available for download
at https://github.com/uraich/IoT4AQ/tree/main/workshop
Please also have a look at the Wiki pages:
https://github.com/uraich/IoT4AQ/wiki

---
What is IoT?
Wikipedia:
The Internet of Things (IoT) describes physical objects (or groups of such objects) with sensors, processing ability, software and other technologies that connect and exchange data with other devices and systems over the internet or any other communication networks

---
IoT
The name “Internet of Things” already suggests that there are two distinct components to it:
- Things, which are represented by sensors and actuators. We therefore must have a means to read out these sensors and to control the actuators. Hardware interfaces are needed for this.
- Internet, we must be able to send data read from the sensors to the Internet and receive commands for the actuators from it. This means that we need a network interwork and the software to run the network protocols.

---
IoT system architecture

---
What is IoT
What is an IoT system composed of?
We need:
- Sensors and actuators
- A processor powerful enough to run the network protocol layers
- A network interface: either Ethernet of WiFi
- Interfaces to the sensors and actuators:
  - General Purpose I/O (GPIO) lines
  - I2C, I2S, SPI, serial interfaces
The cost for the controller should be in a good relation with the cost of the things

---
Micro-processors
Up to the 1970’s computers filled cupboards or even rooms.
Then the micro-processor came onto the market integrating a CPU (Central Processing Unit) onto a single silicon chip.
These devices had no on-chip memory nor on-chip interfaces.
A bus system allowed to connect peripherals.

---
A Micro-processor system
This is how a micro-processor system looked like in the end 1970’s:
- 1 MHz clock
- ~ 2 kB of ROM (EPROM) memory
- 128 bytes of RAM
- Keyboard to enter hex instruction code
- Audio tape to save programs

---
Arduino
Micro-processor only understand binary instruction code and the instruction set differs from one machine to another
High level languages abstract programming and compilers translate the high level code to machine instructions
Since resources on the micro-computer are limited the compiler runs on a different machine (PC).
This is called cross-compilation in contrast to native compilation
The Arduino Software Development Kit (SDK) integrates
- Source code editor
- Compiler
- Up-loader
into a single system (Integrated Development Environment IDE)

---
Arduino Uno
The Arduino SDK was developed for the Arduino board (e.g. Arduino Uno) featuring the
Atmel
- ATMeg328P processor
- 32kB Flash memory
- 2kB SRAM
- 1kB EEPROM
- a number of interfaces
  - GPIO, SPI, I2C, ADC
and a standardized connector for piggy back “shields”

---
… and today? for 10 Euros?
The micro-controller

---
ESP32 network connection
ESP32 network connection

---
which micro-controller?
Question of
- Needs (how much memory, which speed, which interfaces …)
- Budget
- Software environment and programming language
- Previous experience
- Taste
Because of its computing power, its interfaces, its network connectivity and its low price we selected the ESP32

---
Programming the micro-controller
Depending on the processor used, several programming environments are available. For the ESP32 you have:
- esp-idf (ESP integrated development framework) provided by Espressif (not recommended for a beginner programmer)
- The Arduino SDK (Software Development Kit) originally developed for the Atmel Atmega chips but today available for many micro-controllers including the ESP32.
- MicroPython. A stripped down Python-3 interpreter with additional features needed by micro-controllers available for several chips including the ESP32.
In these lectures we use the Arduino SDK

---
Interfacing to the “things”
Interfacing to the “things”
The ESP32 has a big number of interfaces implemented on the chip:
- GPIO pins
- PWM
- Capacitive touch sensor
- I2C (Inter Integrated Circuit) interface
- SPI (Serial Peripheral Interface) interface
- Analogue to digital converter
- Digital to analogue converter
- Timer

---
ESP32 pinout
ESP32 pinout

---
Checking the system
In C the ubiquitous “hello world” program checks if
- You can edit a program
- You can compile and link it
- You can run it
On embedded systems the simplest program possible is often the “blinking led” program
It shows that you can access the system and that interfacing works