Developing an IoT System
IoT Air Quality System
Uli Raich (uli.raich@gmail.com)
The I2C bus
Presented at the Workshop – IoT4AQ
March 2024, Bambey, Sénégal

---
The Inter Integrated Circuit (I2C) bus was invented by Philips in the early 1980s.
It is a synchronous bus using 4 connections:
- Vcc and GND
- SCL: a clock line
- SDA: a data line
It is a master / slave protocol with the ESP32 being the master
We have 2 I2C slaves: DS3231 Real Time Clock and the PCF8574 remote 8 bit expander and the LCD display.

---
The I2C protocol
The I2C protocol transmits a 7-bit slave address + 1 bit R/W. A maximum of
~ 128 slaves can be connected

---
The wire library
The Arduino provides the Wire library with functions giving access to I2C slaves
To find out which slaves are connected to the bus you can send the all 128 addresses onto the bus and check on which address you receive an answer (ACQ)
#include <Wire.h>
…
WIRE.begin();
for (int addr=0;addr<128;addr++) {
WIRE.beginTransmission(addr);
if (!WIRE.endTransmission)
   … there is a slave on this address