Developing an IoT System
IoT4AQ
Uli Raich (uli.raich@gmail.com)
Basic C++ programming
Presented at the Workshop – IoT4AQ
March 2024, Bambey, Sénégal

---
Arduino Template
When you create a new program:
File → New Sketch
this is what you get
The setup() function is executed once
at startup (initialization)
Loop() is executed repeatedly
Set ESP32 Dev Module with
Tools → Board → ESP32
Select the correct serial port with
Tools → Port

---
Variable definition
Before using a variable it must be declared: type variable name
Type can be
- int for integers (or int8_t, int16_t, uint8_t, uint16_t)
- float or double for real numbers
- bool for boolean variables
- char for characters

---
Comments
Comments are not executed but they are very important to explain to the reader what you are doing
// this is a comment
Everything after the // until the end of the line is considered a comment
/*
This is a multi-line comment
when it takes a little more to explain your
extraordinary ideas
*/

---
Serial port
How to see the result of the calculation?
Send the data to the serial interface and observe it on the serial monitor:

---
Compile and execute
The button with the tick mark compiles
you program and checks for syntax errors
The arrow button
- Compiles the program
- Uploads it to the ESP32 if no syntax errors are found
- Resets the CPU to start the program

---
The Serial Monitor
The baud rate must comply to what you set in Serial.begin()

---
Assignments
c = a+b is not a mathematical equation !
”=” is the assignment operator:
a = a+3 makes no sense as an equation but is a valid assignment
        get the value of a, add 3 to it, store it back into a
abbreviation:
a += 3, same for the other operators: - * /
a++ increments a by 1,
a-- for decrement

---
Conditions

---
Conditions (2)
In case of
Serial is a boolean variable which becomes true when the port is ready.
Condition often imply comparison:
<, <=, >, >=, ==, !=

---
while loop
An example calculating factorial of 10:

---
Breaking out of a while loop

---
for loops