IoT Air Quality System
IoT Air Quality System
Jacob Mb. Taamté (mtjfirst@yahoo.fr)
Programming of the Workshop Project
Presented at the Workshop – IoT4AQ
March 2024, Bambey, Sénégal

---
Workshop Project
Workshop Project

---
Connect and test components
Write the operating program for each sensor and electronic component to be used (sensors: PMS5003 and DHT11, components: LCD);
Individually program and test the operation of these sensors ;
Create your account on the Thingspeak platform, customize it and copy the API key;
Write and test the data transmission program (Wi-Fi and Thingspeak) to the Cloud platform by inserting in this program: the API keys, the channel number, the name and password of your personal WiFi;
Gradually merge the programs to obtain a final program of the system;
Compile the programs at each stage and correct errors if they occur;
Assemble the device and upload the final program;
Power the device and check its operation on LCD, Serial monitor of IDE Arduino and the Thingspeak platform.

---
Connect and test components (2)
Connection pinout
LCD I2C 20x4	ESP32 board
SDA	D21
SCL	D22
GND	GND
5V	VIN
Standard connection pinout
PMS5003	ESP32 board
RXD	D17 (TX2)
TXD	D16 (RX2)
GND	GND
5V	VIN
Connection pinout
DHT11	ESP32 board
SIGNAL (Out)	GPIO15 (D15)
GND	GND
5V	VIN

---
Connect and test components (3)
Program to use :
Workshop_demo3.ino : which already summarizes the program of
Thingspeak, Wifi, PMS5003, LCD 20x4 and that of DHT11.

---
Connect and test components (4)
Customization of the system program for its connection to ThingSpeak

---
PM1.0 (µg/m3)
PM2.5 (µg/m3)
Temperature (°C)
Relative Humidity (%)