Developing an IoT System
IoT Air Quality System
Uli Raich (uli.raich@gmail.com)
The DHT11 temperature and humidity sensor
Presented at the Workshop – IoT4AQ
March 2024, Bambey, Sénégal

---
DHT11 sensor
The DHT11 is a popular temperature and humidity sensor
It contains the sensors, analogue to digital conversion and a processor sending the measurement results over its own proprietary serial protocol
It uses only 3 pins:
- Vcc (3.3V)
- GND
- Data

---
The humidity sensor
- Variations in relative humidity produce a change
  of resistivity, which is measured.
- The resistance of certain hygroscopic materials such as
  hygroscopic salts have such a property
- These materials are mounted as thin films on
  the substrate with metal contacts
- The devices can be very small

---
The temperature sensor

---
The connections

---
Communication process
- The processor initiates a measurement cycle pulling the data line down for 18 ms (data line is output to the CPU)
- It releases the line and waits for 20-40 µs (data line now input)
- The DHT11 sends a 80 µs start signal
- 40 data bits follow: 26-28 µs : zero, 70 µs one

---
The full protocol
- Humidity integral
- Humidity decimal
- Temperature integral
- Temperature decimal
- Checksum

---
DHT11 Arduino Library
Getting the DHT11 measurements looks difficult. However, it is possible to write libraries that hide all the protocol details and that provide a small number of functions needed to easily access temperature and humidity values.
The DHT11 library implements DHT11 access as a C++ class.
A class is a data type incorporating data and functions into a single object.
To access the library a definition file must be included.
#include <DHT11.h>
is treated by the gcc pre-processor.

---
Arduino Library Structure
Arduino libraries usually contain
- The source code ( in the src folder) + include file
- A library.properties file specifying
  - its name
  - its author
  - version number
  - on which hardware it runs
- examples

---
DHT11 class methods
- DHT11 DHT11(int data_pin): the object constructor
- void setDelay(ms_delay): sets the delay between 2 measurements (default 500 ms) I need at least 1.2s.
- int readHumidity()
- int readTemperature()
  These methods return the measured values or
  DHT11::ERROR:TIMEOUT (253) or DHT11:ERROR:CHECKSUM (254)
- int readTemperatureHumidity(int &temperature, int &humidity)
  returns 0 if ok, DHT11::ERROR:TIMEOUT (253) or DHT11:ERROR:CHECKSUM (254)
  otherwise
- static String getErrorString(int errorCode): prints a humanly readable error message

---
examples