Iot4AQ workshop exercises
## Exercises on the PlanTower PMS5003 dust sensor
Make the hardware connections according to the table below:
PMS5003 pin number	PMS5003 pin significance	ESP32 GPIO pin number
Pin 1	Vcc	5V
Pin 2	GND	GND
Pin 3	Set (suspend mode)	not used
Pin 4	Rx (serial receive)	GPIO 17
Pin 5	Tx (serial transmit)	GPIO 16
Pin 6	Reset	not used
Pin 7	NC (not connected)

- Install the ESP32:PMS5003 library into your Arduino SDK
- Read the PMS5003 protocol message using the readMsg() method provided by the PMS5003 class. readMsg returns a structure of type pms5003Data.
  Print the values received for pm1.0, pm2.5 and pm10
  Print the message header.
  Print the checksum.
- Read the raw data using the readRaw() and print them with printRaw(). readRaw returns a pointer to the raw data contained in the PMS5003 message. You can use this pointer as a parameter to printRaw()
- Print the checksum as provided by the protocol message and the checksum calculated over the protocol entries and compare them.