## Slide 1: IoT Air Quality System
Uli Raich (uli.raich@gmail.com)
Introduction to Micro-Controllers
Presented at the Workshop – IoT4AQ
March 2024, Bambey, Sénégal

## Slide 2: Resources
These slides are available for download at
https://github.com/uraich/IoT4AQ_B/tree/main/slides

## Slide 3: What is IoT?
Wikipedia:
The Internet of Things (IoT) describes physical objects (or groups of such objects) with sensors, processing ability, software and other technologies that connect and exchange data with other devices and systems over the internet or any other communication networks

## Slide 4: IoT
The name “Internet of Things” already suggests that there are two distinct components to it:
Things, which are represented by sensors and actuators. We therefore must have a means to read out these sensors and to control the actuators. Hardware interfaces are needed for this.
Internet, we must be able to send data read from the sensors to the Internet and receive commands for the actuators from it. This means that we need a network interwork and the software to run the network protocols.

## Slide 5: IoT system architecture

## Slide 6: What is an IoT system composed of?
We need:
Sensors and actuators
A processor, powerful enough to run the network protocol layers
A network interface: either Ethernet of WiFi
Interfaces to the sensors and actuators:
  General Purpose I/O (GPIO) lines
  I2C, I2S, SPI, serial interfaces
The cost for the controller should be in a good relation with the cost of the things

## Slide 7: Micro-processors
Up to the 1970’s computers filled racks or even rooms.
Then the micro-processor came onto the market integrating a CPU (Central Processing Unit) onto a single silicon chip.
These devices had no on-chip memory nor on-chip interfaces.
A bus system allowed to connect peripherals.

## Slide 8: A Micro-processor system
This is how a micro-processor system looked like in the end 1970’s:
1 MHz clock
~ 2 kB of ROM (EPROM) memory
128 bytes of RAM
Keyboard to enter hex instruction code
Audio tape to save programs

## Slide 9: Writing programs
These micro-processors were very limited due to their very small memory footprint.
Micro-processors only understand binary coded instructions and every micro-processor type has its own instruction set. In case of the early microprocessors the memory (and the instruction code) was 8-bits wide. We talk of 8-bit micro-processors.
In case of the M6800 development kit, programs were written in assembly language.
This is a (somewhat) human readable programming language with a one to one correspondence with the binary instruction code. In the first course I gave, we wrote the programs on a piece of paper and translated it into machine code by hand. The machine code was then entered using the keyboard.
There were programs (cross-assemblers) which ran on a big computer and which could do his task automatically.
The first samples of the M6800 micro-processor costed several hundred US$

## Slide 10: High level languages
Assembly language reflects all the details of the micro-processor hardware because you talk directly to registers and memory, which is difficult, and a program written for processor A does not run on processor B
High level languages like Fortran, C, C++, Java, Python … overcome these problems. Programmers writing code in these languages do not need to know the details of the micro-processor hardware. There is a compiler translating the high level code to assembly language for the machine in question and an assembler, which converts the assembly code into machine instructions.
If the compiler runs on the target machine we speak of a native compiler, if it runs on a different machine and is later uploaded to the target, we speak of a cross-compiler.
Today, almost all programs are written in a high level language. The most popular ones for micro-controllers are C or C++.

## Slide 11: Today’s micro-controllers
There are modern micro-controllers which still use 8 bit memory busses like the AVR168 used on the Arduino Uno.
There are two types of memory devices:
RAM: Random access memory
ROM: Read Only memory
In the old times we used EPROMS (Erasable Programmable Read only Memories), which were programmed with a high programming voltage and erased with ultra-violet light.
Today flash memories are used, which are electrically programmable.
Programs can be run off both types of devices but variables must be stored in RAM.

## Slide 12: The AVR168
The Atmel AVR168, used in the Arduino Uno (see later) is a
AVR RISC (Reduced Instruction Set Computer) based CMOS 8-bit micro-controller with
16 KB flash memory
512B EEPROM (Electrically Erasable PROM)
1KB SRAM (Static RAM)
20 MHz typical clock speed
It has a series of interfaces: GPIO (General Purpose Input Output) lines, UART (Universal Asynchronous Receiver Transmitter) for serial communication, Two.Wire serial interface, SPI (Serial Peripheral Interface) serial port, ADC (Analog to Digital Converter)
These additional interfaces make it a micro-controller in contrast to a micro-processor, which has the CPU only.

## Slide 13: Micro-controller speed
The speed at which a micro-controller can executed your programs depends of its clock speed, its instruction set, memory access speed and the width of its memory bus.
As an example:
The ESP32 uses a dual core (2 CPUs on the chip) Xtensa 32-bit LX micro-processor running at 240 MHz
You can imagine that it will run faster than the AVR168, which has only 8 bits and runs at 20 MHz clock speed.
The Raspberry Pi, as a top end processor, has a Broadcom BCM2711, Quad Core Cortex-A72 (ARM v8) 64-bit processor, running at 1.8 GHz.
You can imagine that the price of the processor depends on its performance.

## Slide 14: Software development
Most micro-controller manufacturers provide a Software Development Kit (SDK) for their chips.
These contain
A cross compiler and linker
A build system which automates the compile and link process. Typical build systems are make, cmake, ant, bazel ...
A program to upload the binary code to the micro-controller
Some SDKs have a GUI (Graphical User Interface) into which an editor, the compiler and a debugger are integrated. These are usually called IDEs (Integrated Development Environment)

## Slide 15: Compiler versus Interpreter
While compilers translate the source code into a binary program, which is uploaded to the target hardware, an interpreter translates the code on the fly.
In this case the source code is usually translated into byte code, which is binary code for a virtual machine. The virtual machine, a program that acts like a processor with its own instruction set, converts the byte code into the instruction set of the underlying hardware.
The interpreter must run on the target machine. Since this is a rather big program this method can only be used on targets with more resources.
The programs run slower, but you can execute instructions with writing a full program, which makes debugging substantially easier.

## Slide 16: The Arduino SDK
Programming, even with high level languages is not an easy task. Writing a program requires an editor to produce the source code.
You may have to read a book to fully understand how to use an editor.
C++ is described by its inventor B. Soustrup in another 1000 pages book.
To fully understand the build system, another 250 pages
Then the debugger …
Programming used to be a job for professional.
The Arduino SDK made programming a micro-controller accessible to everybody.

## Slide 17: Arduino IDE

## Slide 18: The Arduino SDK setup
Before we start programming:
The target machine must be selected
The micro-controller must be connected to the development machine on which the SDK is running, through a serial line. Most target machines use an USB to serial converter
The serial port for uploads must be chosen
The baud rate for upload of binary programs the the micro-controller must be selected
Then we can start editing our program

## Slide 19: The Arduino editor

## Slide 20: Writing Arduino programs
The Arduino programming language is a C++ like language. Most C++ constructs are available
Due to the limited resources of the micro-controller some of the libraries are restricted. Printing is a typical example
An Arduino program consist of 2 parts:
A setup function which is executed once. This function performs all initialization needed, including initialization of sensor and actuator devices
A loop function which is run repetitively.
A micro-controller program almost always has an endless loop

## Slide 21: How to get at results
Print the result on the serial line and observe them on the serial monitor

## Slide 22: The data plotter
The is also a plotting function in which data, written onto the serial line, will be displayed in a graph.

## Slide 23: Arduino Uno
The Arduino SDK was developed for the Arduino board (e.g. Arduino Uno) featuring the Atmel
ATMeg328P processor
32kB Flash memory
2kB SRAM
1kB EEPROM
a number of interfaces
  GPIO, SPI, I2C, ADC
and a standardized connector for piggy back “shields”

## Slide 24: Other AVR Arduinos
Arduino Nano
Smaller footprint
Arduino Mega
Uses Atmega2560 processor
Atmega with WiFi interface

## Slide 25: Arduino Shields
Motor controller shield
Multifunction shield
Joypad shield

## Slide 26: Network shields
Ethernet shield
Wifi shield

## Slide 27: The micro-controller

## Slide 28: ESP32 network connection

## Slide 29: Other ESP processors
ESP32 with LCD
ESP32C3
RiscV
ESP32-CAM
ESP32 WeMos
ESP32 S3 with camera
and microphone
ESP32S3
WeMos
ESP32 LoRa

## Slide 30: which micro-controller?
Question of
Needs (how much memory, which speed, which interfaces …)
Network interface?
Budget
Software environment and programming language
Previous experience
Taste
Because of its computing power, its interfaces, its network connectivity and its low price we selected the ESP32

## Slide 31: Programming the micro-controller
Depending on the processor used, several programming environments are available. For the ESP32 you have:
esp-idf (ESP integrated development framework) provided by Espressif (not recommended for a beginner programmer)
The Arduino SDK (Software Development Kit) originally developed for the Atmel Atmega chips but today available for many micro-controllers including the ESP32.
MicroPython. A stripped down Python-3 interpreter with additional features needed by micro-controllers available for several chips including the ESP32.
In these lectures we use the Arduino SDK

## Slide 32: Interfacing to the “things”
The ESP32 has a big number of interfaces implemented on the chip:
GPIO pins
PWM
Capacitive touch sensor
I2C (Inter Integrated Circuit) interface
SPI (Serial Peripheral Interface) interface
Analogue to digital converter
Digital to analogue converter
Timer

## Slide 33: ESP32 pinout

## Slide 34: Checking the system
In C the ubiquitous “hello world” program checks if
You can edit a program
You can compile and link it
You can run it
On embedded systems the simplest program possible is often the “blinking led” program
It shows that you can access the system and that interfacing works

## Slide 35: Micro-controllers running Linux
Raspberry Pi 4 or 5
Luckfox Pico Pro Max

## Slide 36: The Raspberry Pi
The specifications on a previous slide show that the Raspberry Pi is vastly more powerful than all the other micro-controller we have seen before.
In fact the Raspberry Pi should be considered a complete small computer.
It can use a big SD card as its “hard disk” and run a full blown Linux operating system.
It has an HDMI interface onto which you can connect a monitor screen and it has 4 USB interfaces that can be used with a keyboard and a mouse.
This allows to run Linux autonomously and to have a desktop on the connected screen. All Linux programs can be executed and the C, C++ … compilers can be run natively.
The full C-Python interpreter is available and of course all the Linux network capabilities are there.
However, the Raspberry Pi is also a factor 20 more expensive than an ESP32 not counting the price for screen, keyboard and mouse.

## Slide 37: The Raspberry OS screen

## Slide 38: Raspberry Pi interfaces
The Raspberry Pi allows to connect external devices through
GPIO
UART
SPI, I2C or CAN bus
just like the ESP32 or the AVR Arduino boards. It does not have a built-in ADC though.

## Slide 39: Raspberry Pi pinout

## Slide 40: A library to access external devices

## Slide 41: The Luckfox Pico
Just like the Raspberry Pi, the Luckfox Pico can run Linux off an SD card and it has an Ethernet interface.
However, a screen and keyboard and mouse cannot be connected to it.
You can however connect to the Luckfox over the network using ssh and use the X11-forwarding to get the graphical user interface of your applications on the screen of your PC or MAC.
The Luckfox also has a camera interface and it features a processor for AI applications. It is therefore particularly suited for image treatment.
At a price of ~ 20 US$ it is still rather cheap.

## Slide 42: References
The C++ Programming Language, Bjarne Soustrup
Arduino Cookbook. O’Reilly
Developing IoT Projects with ESP32, Bedat Ozan Oner
https://afnog.iotworkshop.africa/do/view/Main/WebHome (embedded systems with Raspberry Pi (C- language), IoT with ESP32 using MicroPython