Internet of Things Lab for Air quality Monitoring (IoT4AQ) / International Workshop – Air Quality & IoT-based Air Sensors / 14-15 March 2024, Alioune Diop University, Senegal

IoT4AQ Workshop Exercises

## Exercises on the 2004 LCD
The 2004 LCD can display 4 rows of 20 characters each.
- Write the following text to the display:
  Welcome to the
  IoT4AQ workshop 2024
     Alioune Diop
  University, Bambey
- Read the temperature and humidity from the DHT11
  Read the pm1.0, pm2.5 and pm10 values from the PMS5003
  Print the results on the display in the following format:
  Temperature: 22deg
  Humidity: 56%
  pm1.0: 5 pm2.5: 6
  pm10: 10

Too easy?
Replace “deg” in the second program by °C. The “°” character does not exist in the ROM character table but can be added as a user defined character.