Internet of Things Lab for Air quality Monitoring (IoT4AQ) / International Workshop – Air Quality & IoT-based Air Sensors / 14-15 March 2024, Alioune Diop University, Senegal

IoT4AQ Workshop Exercises

## Exercises on the 2004 LCD
The 2004 LCD can display 4 rows of 20 characters each.
Exercise 1:
Write the following text to the display:
Welcome to the
IoT4AQ workshop 2024
Alioune Diop
University, Bambey

Internet of Things Lab for Air quality Monitoring (IoT4AQ) / International Workshop – Air Quality & IoT-based Air Sensors / 14-15 March 2024, Alioune Diop University, Senegal

Exercise 2:
Read the temperature and humidity from the DHT11
Read the pm1.0, pm2.5 and pm10 values from the PMS5003
Print the results on the display in the following format:
Temperature: 22deg
Humidity: 56%
pm1.0: 5 pm2.5: 6
pm10: 10

Too easy?
Exercise 3:
Replace “deg” in the second program by °C. The “°” character does not exist in the ROM character table but can be added as a user defined character.

Internet of Things Lab for Air quality Monitoring (IoT4AQ) / International Workshop – Air Quality & IoT-based Air Sensors / 14-15 March 2024, Alioune Diop University, Senegal